## Slide 1
Jordan J. Gerth
Assistant Researcher, Liaison to NWS Pacific Region
Cooperative Institute for Meteorological Satellite Studies
University of Wisconsin at Madison
Timothy J. Schmit
Research Meteorologist
National Environmental Satellite, Data, and Information Service
Bill D. Ward
Environmental and Scientific Services Division Chief National Weather Service Pacific Region Headquarters
Includes contributions from the community
GOES-R: What it means for the operational meteorologist
National Weather Association 2015 Broadcast Meteorology Workshop Edition

## Slide 2: GOES-R spacecraft and solar panel

## Slide 3: An update on GOES-R/S launch
GOES-R is tentatively scheduled to launch on October 14, 2016, in Cape Canaveral, Florida
GOES-S will launch approximately one year after the GOES-R launch
Post-launch testing will occur at 89.5 W and GOES-R will be positioned there for approximately one year
Operational location of GOES-R will depend on NWS priorities and the health of the existing GOES satellites

## Slide 4
Launch & Orbit Raising
Operations -
Post-launch Testing (PLT) - 180 Days
Outgas
System Performance Operational Test (SPOT)
12 Days
30 Days
60 Days
6 Mo
30 Days
PLPT
Ex-tended Val
<=5yrs Storage + >=8.4yrs Ops
PLT Cal/INR
32 Days
28 Days
09 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31 | 32 | 33 | 34 | 35 | 36
GOES West
On-orbit spare
GOES East
Fiscal Year
On-orbit storage
Operational
GOES-13
GOES-14
GOES-15
GOES-R
GOES-S
GOES-T
GOES-U
Test & Checkout
Fuel-Limited Lifetime
Post-launch Calibration, Instrument Navigation and Registration
Post-launch Product Testing
Continuity of GOES through 2036
Lockheed Martin

## Slide 5: Future GOES-R/S constellation

## Slide 6: Advanced Baseline Imager (ABI)
5
4
3
X
Faster scanning (5-minute full disk vs. 25-minute)
X
Improved spatial resolution (2 km IR vs. 4 km)
X
More spectral bands (16 on ABI vs. 5)

## Slide 7: Other instruments
EXIS
Extreme Ultra Violet /
X-Ray Irradiance Sensor
Detects solar x-ray output
GLM
Geostationary Lightning Mapper
Detects lightning
MAG
Magnetometer
Measures the space environment magnetic field
SUVI
Solar Ultra Violet Imager
Monitors the sun for solar flares and eruptions of filaments that may precede coronal mass ejections
SEISS
Space Environmental In-Situ Suite
Measures proton, electron, and heavy ion fluxes to mitigate radiation risks to astronauts and damage to radio communication

## Slide 8: Two talks on GOES-R
Today
  Possible uses for GOES-R meteorological imagery and products as part of television segments and online content, geared toward broadcast meteorologists
Tomorrow
  How the Advanced Baseline Imager (ABI) can improve detectability of unique weather events and impact weather forecast decisions, with examples from the Advanced Himawari Imager (AHI)
Japan Meteorological Agency Mascot “Harerun”

## Slide 9: Improved spatial resolution
Highest infrared window spatial resolution from two GOES-R series satellite constellation

## Slide 10: Improved spatial resolution

## Slide 11: Improved spatial resolution

## Slide 12: Pseudo-natural color imagery
Psuedo-natural color image with a “synthetic” green band from CIMSS-simulated ABI data. Source: Don Hillger, RAMMB.

## Slide 13: One-minute imagery
Instrument: Advanced Baseline Imager
Animations of one-minute imagery make boundary interactions, morning low cloud decay, convective development, and overshooting tops visually evident

## Slide 14: Lightning density
Instrument: Geostationary Lightning Mapper
Integrate lightning density with satellite imagery from the ABI to depict intense thunderstorms
Right: Tornado tracks in red

## Slide 15
An example of data fusion in use at NWS offices today
Object-tracking in both GOES and radar imagery
Predictors from GOES-derived cloud products, MRMS products, and RAP-derived fields
Use trained statistical model to compute probability of future severe weather:
IA
MO
P(severe) = f (GOES, RAP, MRMS) + lightning
NOAA/CIMSS ProbSevere Model
http://cimss.ssec.wisc.edu/severe_conv/probsev.html

## Slide 16: Ask your vendor…
…about the types of products and graphics that will be available in the GOES-R era
  Routine imaging
  Mesoscale imaging
    Severe thunderstorms
    Tropical cyclones
  Space weather products
…when GOES-R imagery and products will be available to you in relation to launch
…how they plan to handle the data rate

## Slide 17: Baron plan for GOES-R rollout
Will operate GOES-R receiver on-site at Baron HQ in Huntsville, Alabama
Plan to initially make use of ABI (Advanced Baseline Imager) and GLM (Geostationary Lightning Mapper)
Since GOES-R will produce an order of magnitude more data than current generation, we must work to solve client-end bandwidth constraints by packing GOES-R data via most efficient compression methods available
Baron was the first to use GOES-14 SRSO natively in our weather display software (October 2012 – Hurricane Sandy) Here was Hurricane Danny on August 21, 2015 in Baron OMNI software:
Slide
courtesy
of

## Slide 18: Learn more: Short courses
AMS Annual Meeting short course on GOES-R
  New Orleans, Louisiana
  January 10, 2016
  Participation cost is $50
Bring a laptop computer or tablet for interactive exercises
Other similar short courses planned (pending approval)
  2016 AMS Conference on Broadcast Meteorology
  2016 NWA Annual Meeting

## Slide 19: Learn more: Web applications
http://cimss.ssec.wisc.edu/education/goesr/

## Slide 20: Points of emphasis
GOES-R is the most significant improvement to United States geostationary weather satellites in over 20 years.
The GOES-R ABI will improve detectability of subtle changes in the state of the atmosphere with increases to spatial, spectral, and temporal resolution.
Optical cloud-top lightning information from the GOES-R GLM will help assess storm severity.

## Slide 21
Thank you!
For more information, visit www.goes-r.gov
or e-mail
Jordan.Gerth@noaa.gov
www.facebook.com/GOESRsatellite
www.youtube.com/user/
NOAASatellites
twitter.com/NOAASatellites
www.flickr.com/photos/
noaasatellites