## Slide 1
John Cintineo (UW-CIMSS)
Michael Pavolonis (NOAA/NESDIS)
Justin Sieglaff (UW-CIMSS)
2021 NOAA AI Workshop
14 September 2021
Acknowledgement: GOES-R program
Evaluating and exploring lightning predictions from NOAA/CIMSS ProbSevere LightningCast

## Slide 2
Question: Can we provide accurate and timely lightning guidance using satellite imager data?
Lightning is hazardous for aviation, mariners, and outdoor events and activities.
  Geostationary satellite data can provide observations of clouds prior to electrification (CI guidance).
  The data can respond to changes in storm structure before radar (e.g., storm intensification or decay).
Credit: NOAA

## Slide 3
Methods and Data
LightningCast model: U-Net architecture
  Learns salient spatial, multispectral features from images; image-to-image translation
Predictor channels (GOES-16 ABI):
  0.64-µm reflectance (CH02)
  1.6-µm reflectance (CH05)
  10.3-µm brightness temperature (CH13)
  12.2-µm brightness temperature (CH15)
  Still exploring other predictor channels
Target/truth: GLM flash-extent density
  Accumulated from t0 to t0 + 60 min
  Binarized at 1 flash
Output: Pixel-by-pixel probability ≥ 1 GLM flash in the next 60 min

## Slide 4
Notes: Sea-breeze example

## Slide 5
Notes: Early morning example with thick cloud cover

## Slide 6
Notes: Meso example with some overlapping clouds

## Slide 7
P(LTG) ≥ 25% 51 min prior to first flash
P(LTG) ≥ 50% 43 min prior to first flash
P(LTG) ≥ 75% 30 min prior to first flash
First flash
at 20:30 Z

## Slide 8
Notes: Meso example with mid-level cloud deck. Still good lead-time.

## Slide 9
Notes: Nothing specific to point out here. Just a regional example.

## Slide 10
Notes: Nothing specific to point out here. Different regime and sat viewing angle.

## Slide 11
Training and validation data
Training/validation domain: 5 patches from GOES-16 ABI CONUS sector
  76,031 training samples
  22,539 validation samples

## Slide 12
Test data
GOES-16 CONUS sector
5 days of 5-min scans from each month of 2020

## Slide 13
GOES-16

## Slide 14
GOES-16

## Slide 15
GOES-16

## Slide 16
GOES-16
Good
Needs improvement

## Slide 17
Layer-wise Relevance Propagation
“Layer-wise Relevance Propagation (LRP) is a technique that brings such explainability and scales to potentially highly complex deep neural networks. It operates by propagating the prediction backward in the neural network, using a set of purposely designed propagation rules.” – Montavon et al. (2019)
LRP propagates the prediction backward to input pixels of each channel.
LRP is subject to a conservation law, whereby what is received by a neuron must be distributed to the lower layer in equal amount.
We’re using LRP-Z rule from innvestigate github.

## Slide 18
Layer-wise Relevance Propagation

## Slide 19
“X” is NW-corner of pixel of interest
Bright pixels nearby help elevate probability when cloud is not cold enough
Bright pixels helping
Cold cloud pixels in CH15
WARM surface pixels in CH13
Predicted probability at pixel X

## Slide 20
Wrap up
LightningCast is a CNN (U-Net) that predicts lightning (as observed by GLM) up to 60 min in the future
  Inputs: ABI CH02, CH05, CH13, CH15
ABI alone can provide skillful short-term prediction for lightning (including LI), day and night, over land and sea. Very fast to compute.
  Daytime a little better than nighttime
  Over land a little better than over ocean
Lead-time for LI events often ranges between 10 and 30 minutes.
Near-real-time output: https://cimss.ssec.wisc.edu/severe_conv/pltg.html
  GOES-16 and GOES-17 CONUS and MESO sectors
Future work:
  Use more training data!
  Evaluate more channels (e.g., water vapor channels)
  Investigate training models with different lead-time and flash rate criteria

## Slide 21
Input
Conv 3x3 + ReLU
Max-pooling
Upsampling
Concatenation
Conv 1x1 + Sigmoid
4
16
32
128
64
256
128
64
32
16
1
values indicate layer depth
Model: Semantic segmentation, or “U-Net” (Ronneberger et al. 2015)