## Slide 1
Nested Global and Regional Scale Modeling of the Impacts of Intercontinental Pollution Transport and Stratospheric Intrusion on Surface Air Quality in the Western US
R. Bradley Pierce1, Todd Schaack2, Allen Lenzen2, Andrew Wentland3, Georg Grell4, Steve Peckham4, Emma Yates5, Laura Iraci5, Thomas McGee6, John Sullivan7
1NOAA/NESDIS/STAR
2UW-Madison/SSEC
3UW-Madison/AOS (Now at ENVIRON)
4NOAA/ESRL
5NASA Ames
6NASA/GSFC
7UMBC/JCET
Meteorology And Climate - Modeling for Air Quality (MAC-MAQ), September 16-18 2015, Sacramento, CA

## Slide 2
Can nested global/regional ozone predictions help inform Stratospheric Intrusion (SI) Exceptional Event and Intercontinental Transport 179B demonstrations?
Nested RAQMS1/WRF-CHEM2 Configurations
  1x1 degree RAQMS global ozone analysis
    Unified stratosphere/troposphere chemistry/GOCART aerosols
    UW-Hybrid sigma-theta dynamical core
    Constrained with Microwave Limb Sounder (MLS) stratospheric ozone profiles and Ozone Monitoring Instrument (OMI) cloud cleared Total Column Ozone
  12km WRF-CHEM v3.4.1 (Eastern Pacific Domain)
    GOCART RACM-KPP mechanism
    YSU PBL scheme (Yonsei University, Non-local-K scheme)
  13km NOAA/ESRL RR-CHEM (North American Domain)
    RADM2 chemical mechanism/MADE Aerosol parameterization
    YSU PBL scheme (Yonsei University, Non-local-K scheme)
1Realtime Air Quality Modeling System (RAQMS, http://raqms.ssec.wisc.edu/)
2Weather Research and Forecasting (WRF) model with chemistry (WRF-CHEM, http://ruc.noaa.gov/wrf/WG11/)

## Slide 3
“The Wyoming Department of Environmental Quality/Air Quality Division (WDEQ/AQD) has determined that a stratospheric intrusion created elevated ozone readings resulting in an 8-hour ozone standard exceedance at the Thunder Basin, Wyoming ozone monitor located in northeastern Wyoming on June 6, 2012” (Executive Summary)
Thunder Basin Wyoming
Ozone Standard Exceedance
June 6, 2012
Yates, et al. 2013, Atmos. Chem. Phys., 13, 12481–12494, 2013, www.atmos-chem-phys.net/13/12481/2013/ doi:10.5194/acp-13-12481-2013

## Slide 4
Figures courtesy Patrick Reddy (Colorado Department of Public Health and Environment)
Synoptic conditions prior to Thunder Basin, WY ozone exceedance
June 5, 2012 NAM-12 analysis, 11 am MST
June 6, 2012 NAM-12 analysis, 11am MST
Thunder Basin, WY
Thunder Basin, WY
Legend:
500 mb heights in meters (contours)
600 mb IPV >= 1.5 PVUs (blue)
600 mb RH <= 10% (grey)
EPA AQS Daily Max 8-hour O3 in ppb >= 65 ppb (rainbow contours and shading)
High Isentropic Potential Vorticity (IPV) and low relative humidity (RH) at base of large amplitude trough over CA/NV on June 5 is associated with high surface ozone over SW Utah on June 5 and NE WY on June 6, 2012

## Slide 5: Alpha Jet Atmospheric eXperiment (AJAX) (Emma Yates and Laura Iraci, NASA Ames)
Description:
Based at and operated from Moffett Field, CA
Flight duration:
Approximately 2.5 hrs
Measurements:
O3, CH4, CO2, water vapor
O3 Mission San Joaquin Valley/Off Shore
5 June 2012
https://espo.nasa.gov/missions/ajax/content/AJAX
  Filament of high (>190ppbv) O3 sampled during onshore profile

## Slide 6
Back-trajectory analysis shows that the origin of the SI event was within a region of high total column ozone over the Gulf of Alaska
Origin of the tropospheric fold and subsequent Stratospheric Intrusion (SI)
Backward trajectories (white) beginning at the AJAX Flight 47 path, and ending on May 30, 2012 (blue) overlayed on mean AIRS total column ozone
RAQMS ozone analysis at 150º W at 18Z on May 30, 2012 combined with the location of the SI trajectories on May 30, 2012 (blue)

## Slide 7
  310K O3 from RAQMS/WRF-CHEM Simulation
  00Z 05/30 – 00Z 06/07, 2012
  Stratosphere/tropospheric exchange processes within a quasi-stationary low pressure system over the Gulf of Alaska played a critical role in the SI event

## Slide 8
  310K O3 from RAQMS/WRF-CHEM Simulation
Southeasterly transport of stratospheric air along the 310K isentropic surface leads to the SI event sampled by the AJAX flight over CA on June 5, 2012

## Slide 9
RAQMS
Nested RAQMS/WRFCHEM
310K isentrope
NASA AJAX Flight 47, June 5, 2012
Nested RAQMS/WRFCHEM simulations significantly improve the agreement with AJAX measurements during the off-shore spiral (B) but still underestimate ozone within the narrow filament sampled during the spiral over the San Joaquin Valley, CA (A)
(A)
(B)
(A)
(B)
RAQMS (red)
AJAX (black)
WRFCHEM (red)
AJAX (black)

## Slide 10
Improved estimates of ozone within the SI event lead to significant improvements (19.3 vs 31.8ppbv daytime bias) in predictions of ozone at the Thunder Basin, WY surface site in the nested RAQMS/WRF-CHEM simulation.
However, peak ozone mixing ratios are still underestimated by nearly 30ppbv
June 6-7, 2012 Surface ozone comparison: Thunder Basin, WY
Surface O3 from AIRNow and Nested RAQMS/WRF-CHEM
Surface O3 from AIRNow and RAQMS
RAQMS
Nested RAQMS/WRFCHEM
RAQMS (red)
AIRNow (black)
WRFCHEM (red)
AIRNow (black)

## Slide 11
RAQMS/RR-Chem Real-time forecasts during the 2014 FRAPPE/DISCOVER-AQ mission
Nested RAQMS/RR-Chem forecasts show reduced biases and improved variability compared to airborne insitu measurements between 700-500mb.
However, biases are similar (15-20 ppbv) below 700mb and neither model captures the upper 90% of the observed ozone
Reduced bias

## Slide 12
NASA Goddard Space Flight Center TROPospheric OZone DIfferential Absorption Lidar (GSFC TROPOZ DIAL)
(Thomas McGee, GSFC and John Sullivan UMBC)

## Slide 14
RR-CHEM shows improved correlation, reduced bias, and similar RMS errors compared to 1 degree RAQMS analysis

## Slide 15
July 16 – August 17, 2014 RR-Chem Ozone timeseries
(Fort Collins, CO)

## Slide 16
August 6: STE
July 16 – August 17, 2014 RR-Chem Ozone timeseries
(Fort Collins, CO)
John T. Sullivan et al., 2015, under review, JGR

## Slide 17
August 06, 2014 TROPOZ and RR-Chem Ozone timeseries
(Fort Collins, CO)
RR-CHEM captures altitude of STE and low ozone tropical air aloft but underestimates the ozone mixing ratio within the STE

## Slide 18
August 6: STE
August 9: CONUS PBL
July 16 – August 17, 2014 RR-Chem Ozone timeseries
(Fort Collins, CO)

## Slide 19
August 6: STE
August 9: CONUS PBL
July 16 – August 17, 2014 RR-Chem PAN timeseries
(Fort Collins, CO)

## Slide 20
RAQMS Reverse Domain Filling (RDF) show that high PAN airmass over Fort Collins on 08/06 had it’s origins within the Continental US boundary layer
Pierce, R. B. 2008, J. Geophys. Res., 114, D00F09, doi:10.1029/2008JD011337

## Slide 21
August 6: STE
August 9: CONUS PBL
August 11:East Asian Transport
July 16 – August 17, 2014 RR-Chem PAN timeseries
(Fort Collins, CO)

## Slide 22
RAQMS RDF shows that high PAN air mass over Fort Collins on 08/11 had it’s origins within the East Asian boundary layer

## Slide 23
330K Nested
RAQMS/RR-CHEM
O3 (colored)
PAN (Black contours)
Surface intersection
(White)
320K Nested
RAQMS/RR-CHEM
O3 (colored)
PAN (Black contours)
Surface intersection
(White)
Discontinuity at LBC due to animation of RAQMS Analysis (forecast used in nesting)

## Slide 24
Backup Slides

## Slide 25
August 6: STE

## Slide 26
August 9: CONUS

## Slide 27
August 11: EASIA