## Slide 1: Advances in Real-time Assimilation of Satellite Trace Gas and Aerosol Retrievals for Air Quality Forecasting R. Bradley Pierce NOAA/NESDIS/STAR
08Z 4/17 2010
11 mm AOD
NWS Western Region SOO/DOH Call:
Wed 9 April - 1000 MDT/0900 PDT

## Slide 2
NWS National Air Quality Forecasting Capability (NAQFC) provides operational predictions* of ozone and wildfire smoke nationwide and operational predictions of airborne dust over the contiguous 48 states.
Background
From Ivanka Stajner (NAQFC NWS Manager) AMS Annual Meeting, Atlanta, GA, February 5, 2014
*Using the US EPA Community Multi-scale Air Quality (CMAQ) model for ozone and the NOAA Hybrid Single Particle Lagrangian Integrated Trajectory (HYSPLIT) for smoke and dust
Improving the basis for air quality alerts
Providing air quality information for people at risk

## Slide 3
The NOAA Environmental Modeling System (NEMS) Global Forecast System (GFS) Aerosol Component (NGAC) currently provides operational dust forecasts* globally. Dust forecasts will be expanded to include sulfate, black and organic carbon, and sea salt during Q2FY15 [Sara Lu, personnel communication]
Background (continued)
http://www.emc.ncep.noaa.gov/gmb/sarah/NGAC/html/realtime.ngac.html
*Using the Goddard Chemistry Aerosol Radiation and Transport Model (GOCART) [Chin et al., 2002] for aerosol predictions.
Allows aerosol impacts on medium range weather forecasts (GFS/GSI) to be considered
Provides a first step toward an operational aerosol data assimilation capability at NOAA
Provides lateral aerosol boundary conditions for regional aerosol forecast system

## Slide 4
Advances in real-time trace gas and aerosol assimilation within the Real-time Air Quality Modeling System (RAQMS)
Collaborative NESDIS/NWS/ESRL real-time nested global/regional air quality forecasting
Focus of this presentation

## Slide 5
Online global chemical and aerosol assimilation/forecasting system
Real-time assimilation:
  Microwave Limb Sounder (MLS) stratospheric ozone profiles (above 50mb)
  Ozone Monitoring Instrument (OMI) total ozone column (cloud cleared)
  Moderate Resolution Imaging Spectroradiometer (MODIS) Aerosol Optical Depth (AOD)
Real-time fire detection:
  Moderate Resolution Imaging Spectroradiometer (MODIS)
UW-Madison sigma-theta hybrid coordinate model (UW-Hybrid) dynamical core
Unified stratosphere/troposphere chemical prediction scheme (LaRC-Combo) developed at NASA LaRC
Aerosol prediction scheme (GOCART) developed by Mian Chin (NASA GSFC).
Statistical Digital Filter assimilation system developed by James Stobie (NASA/GFSC)
http://raqms-ops.ssec.wisc.edu/
RAQMS has been used to develop capabilities to assimilate global satellite composition measurements and support airborne field missions

## Slide 6
NOAA and the California Air Resources Board (CARB) conducted CalNex during (May-June 2010) to investigate the interactions between air quality and climate change issues.
http://www.esrl.noaa.gov/csd/calnex/
NOAA CalNex Field Mission
CalNex-2010 O3 sondes
Owen Cooper (NOAA ESRL)

## Slide 7
Comparison with NOAA P3 Insitu O3 Measurements
(Primarily LA Basin/Central Valley)
Assimilation of MLS+OMI O3 retrievals results in increased lower-tropospheric O3 (and improved agreement with airborne insitu O3) over Southern California
No Assim
MLS+OMI Assim
Insitu O3 from Tom Ryerson, NOAA ESRL
NOAA P3 Flight Tracks

## Slide 8
Evaluation of Real-time AQ Model Forecasts during CalNex
Lead by Stu McKeen (NOAA/ESRL)
Regional Air Quality Forecast models:
Georg Grell, Steven Peckham (NOAA/ESRL/GSD) -WRF/Chem
Wanmin Gong, Sylvain Ménard, Hugo Landry (Environment Canada) – GEM-MACH
Youhua Tang and Jeff McQueen (NOAA/NWS) - CMAQ/NAM (CB-05 - experimental in 2010)
John McHenry and Don Olerud (Baron AMS) – BAMS
From Stu McKeen (NOAA/ESRL) AGU Annual Meeting, San Francisco CA, December, 2010

## Slide 9
Evaluation of Real-time AQ Model Forecasts during CalNex
Lead by Stu McKeen (NOAA/ESRL)
RAQMS used for O3 and PM2.5 lateral boundary conditions (LBC) in NWS CMAQ/NAM and ESRL WRF/Chem
Regional Air Quality Forecast models:
Georg Grell, Steven Peckham (NOAA/ESRL/GSD) -WRF/Chem
Wanmin Gong, Sylvain Ménard, Hugo Landry (Environment Canada) – GEM-MACH
Youhua Tang and Jeff McQueen (NOAA/NWS) - CMAQ/NAM (CB-05 - experimental in 2010)
John McHenry and Don Olerud (Baron AMS) – BAMS
From Stu McKeen (NOAA/ESRL) AGU Annual Meeting, San Francisco CA, December, 2010

## Slide 10
CMAQ/RAQM-LBCs at Joshua Tree
NAM-CMAQ does not resolve sharp gradient in ozone at tropopause resulting in higher ozone in free troposphere
Model
Obs.
From Stu McKeen (NOAA/ESRL) AGU Annual Meeting, San Francisco CA, December, 2010

## Slide 11
CMAQ/NAM
CMAQ/NAM with RAQMS LBC
http://www.esrl.noaa.gov/csd/modeleval/
Real-time CMAQ/NAM 0-1.5km Ozone Forecast 22Z July 15, 2010
Higher free tropospheric ozone leads to increased surface ozone

## Slide 12
Median Model to Observed Ratio
max 8-hr average O3 , 5/19/10 - 7/15/10
CMAQ, no RAQMS-LBC
CMAQ, with RAQMS-LBC
Main impact of boundary conditions is further east
From Stu McKeen (NOAA/ESRL) AGU Annual Meeting, San Francisco CA, December, 2010
Increased surface ozone leads to model high bias along CA/NV boarder

## Slide 13
Retrospective 4km WRF-CHEM CalNex forecasts
(RAQMS 1x1 MLS+OMI ozone analyses)
WRF-CHEM does resolve sharp gradient in ozone at tropopause resulting in very small (<10%) biases in free tropospheric ozone
= EPA AIRNow Surface ozone measurements

## Slide 14
MODIS True Color Image April 7, 2014
https://earthdata.nasa.gov/labs/worldview/

## Slide 15
MODIS Aerosol Optical Depth (AOD) April 7, 2014
https://earthdata.nasa.gov/labs/worldview/

## Slide 16
Current real-time RAQMS air quality analysis/forecasts
Aerosol Optical Depth (AOD)
http://raqms-ops.ssec.wisc.edu/

## Slide 17
AIRS Carbon Monoxide (CO) Column April 7, 2014
https://earthdata.nasa.gov/labs/worldview/

## Slide 18
310K Carbon Monoxide (CO)
Current real-time RAQMS air quality analysis/forecasts
http://raqms-ops.ssec.wisc.edu/

## Slide 19
http://raqms-ops.ssec.wisc.edu/
Current real-time RAQMS air quality analysis/forecasts

## Slide 20
Current real-time RAQMS air quality analysis/forecasts
http://raqms.ssec.wisc.edu/

## Slide 21
The Rapid Refresh (RAP) model with chemistry is used to predict air pollution over CONUS twice daily (00Z and 12Z) using RAQMS forecasts for lateral boundary conditions.
RAP is based on the Weather Research and Forecasting (WRF) coupled with chemistry via the RACM chemical mechanism including MOSAIC/VBS for better prediction of secondary orangic aerosols (SOA).
RAQMS/Rapid Refresh (RAP) with Chemistry
Real time weather and air quality forecasts
http://rapidrefresh.noaa.gov/

## Slide 22
  http://ruc.noaa.gov/wrf/WG11_RT/
ppbv
RAQMS/RAP-Chem 500mb O3 Forecast
00Z April 08 –
00Z April 10, 2014

## Slide 23
  http://ruc.noaa.gov/wrf/WG11_RT/
ppbv
RAQMS/RAP-Chem Surface O3 Forecast
00Z April 08 –
00Z April 10, 2014

## Slide 24
Conclusion
Assimilation of trace gas and aerosol retrievals within a global chemical and aerosol data analysis system can provide improved constraints on the impacts of intercontinental pollution transport and stratosphere/tropospheric exchange processes on regional scale air quality predictions.
Future global operational trace gas and aerosol data assimilation/forecasting at NOAA could follow the EU GEMS/MACC path, where aerosol and chemical DA and forecasting is incorporated into the ECMWF global Integrated Forecasting System (IFS).